RL paper Specifics

State: All vehicles approaching on lanes Vi within 150 meters

Action: Change to next phase, each phase

Reward: sum of all Queued vehicles, definition of Queued is >.1 m/s

Algorithms to use
- Q-learning
- SARSA
- Expected SARSA
- fixed time interval

Paramerters to tune
- learning rate (alpha)
- always use .05
- values .1 .05 .01 and a decreasing function
- exploration value (epsilon)
- always use .05
- values .1 .05 .01 and a decreasing function
- discount factor
- always use .80
- values 0, .5 .75 .8 .9 .95

Intersection Description
- using SUMO
- 4-way intersection
- 1 incoming and outgoing lanes of 300 meters

Phase description
NS and EW they both have three second yellow lights

Traffic
- cars only go EW or NS
- 1
- .033/3 cars/s WE 0 → 7200
- .033/3 cars/s NS 0 → 7200
- 2
- .4/3 cars/s WE 0 → 3600
- .4/3 cars/s NS 3601 → 7200
- 3
- .2/3 cars/s WE 0 → 7200
- .033/3 cars/s NS 0->7200

State:
# of vehicle on appraching lanes

reward:
sum of Queue vahicles that have speed <= .1m/s
Evaluation is time on road

Results

Traffic Patterns

Configuration	Direction	Rate (cars/s)	Start Time (s)	End Time (s)
1	WE	.011	0	7200
1	NS	.011	0	7200
2	WE	.133	0	3600
2	NS	.133	3601	7200
3	WE	.066	0	7200
3	NS	.011	0	7200

Results
Exploration of Discount values for Configuration 1
Alpha and epsilon values are .1 .1
Method	Discount	Avg Travel Time (s)
Fixed Time	NA	161.64
QLearning	0	162.19
QLearning	.5	159.91
QLearning	.75	160.00
QLearning	.8	160.01
QLearning	.9	160.23
QLearning	.95	160.21
QLearning	1	160.40

Exploration of epsilon values for Configuration 1
Alpha and discount values are .1 and .5 respectfully
Method	Epsilon value	Avg Travel Time(s)
Fixed Time	NA	161.64
QLearning	1	162.08
QLearning	.5	161.46
QLearning	.1	159.91
QLearning	.05	161.38
QLearning	.01	160.18
QLearning	0	160.6

Exploration of the learning rate for configureation 1
Epsilon and discount factor are constant at .1 and .5 respectfully
Method	Learning rate	Avg Travel Time(s)
Fixed Time	NA	161.64
QLearning	1	161.49
QLearning	.5	160.63
QLearning	.1	159.91
QLearning	.05	160.57
QLearning	.01	160.39
QLearning	0	162.08

Exploaraton of state aggregation for Configuration 2
All instances has their hyper parameters tuned for near optimal performance

Method	State Aggregation Technique	Avg Travel Time (s)
Fixed Time	NA	179.74
QLearning	No state aggregation	339.61
QLearning	Log function	176.68
QLearning	Min function	171.41

Exploration of state for configuration 3

Exploration of Decreasing learning rate

Exploration of Decreasing epsilon

References
Hua Wei, Guanjie Zheng, Huaxiu Yao, and Zhenhui Li. 2018. IntelliLight:
A Reinforcement Learning Approach for Intelligent Traffic Light Control.
In KDD ’18: The 24th ACM SIGKDD International Conference on Knowledge
Discovery & Data Mining, August 19–23, 2018, London, United Kingdom. ACM,
New York, NY, USA, 10 pages. https://doi.org/10.1145/3219819.3220096

Guanjie Zheng, Xinshi Zang, Nan Xu, Hua Wei, Zhengyao Yu, Vikash Gayah, Kai Xu, and Zhenhui Li. 2019b. Diagnosing Reinforcement Learning for Traffic Signal Control. arXiv preprint (2019).